## Slide 1
IN 1900 (ICT Project)
AUTOMATIC BOXING TRAINING MACHINE
Group No : 40

## Slide 2: Group Members
 | Name | Reg.No. | Photo
Group Leader | Siriwardena P.T.Y. | 204203K | 
Member 1 | Gamage T.T.P.D. | 204059X | 
Member 2 | Kavishka T.A. | 204101V | 
Member 3 | Nuska M.F.F. | 204145H | 
Member 4 | Ekanayaka Y.M | 204239B | 

## Slide 3: Problem in brief
In sports involving only two players, there is a barrier for them to practice on their own. Boxing is that kind of a sport. Always player can’t have a coach, because of having a coach is very expensive and coach can’t hang with us always. When the player is practicing with a coach he has to limit only to coach’s knowledge. Training alone is not successful and also, it’s essential to train with the right techniques to produce a good player.

## Slide 4: Brief Introduction on Boxing
What is Boxing?
  Boxing is a combat sport in which two competitors try to hit each other with their glove-encased fists while trying to avoid each other’s punches.
What is a Punch?
  A punch is a striking blow with the fist.

## Slide 5: There are four main punches in boxing
Jab — a quick, straight punch thrown with the lead hand
Cross — a powerful straight punch thrown with the rear hand
Hook — a semi-circular punch thrown with the lead hand to the side of the opponent's head
Uppercut — a vertical, rising punch thrown with the rear hand
the boxer should join them together in proper order to build combinations.

## Slide 6: Basic Boxing Moves
Slip
The slip is an effective defensive head movement intended to get you out of the path of an oncoming straight punch from your opponent. Slipping can cause your opponent to miss their punch while, in turn, putting your body in balance for a counter punch.
Roll
The roll is another effective defensive movement used to avoid your opponent's hooks by bending your knees and shifting the weight from the lead side to the backside, and vice versa (rolling in vs. rolling out).

## Slide 7
  What is a Boxing Combo (Combination)?
  A boxing combo is a sequence of punches and movements that player execute to attack their opponent.
  Why Need Combinations?
  It doesn’t make sense to throw a single punch because opponent boxing player cannot stop by using a single punch. So, boxers always use punch combinations to hit the opponent.

## Slide 8: What is the Importance of Practicing Combinations?
  Boxers don’t have much more time think about the punches while in the game.
How They Practice Boxing?
  Player should have clear understanding about the combinations (steps of the combination) and he can practice those combinations with the help a coach and it will help the player to develop his muscle memory.
  https://www.youtube.com/watch?v=6VBIuqjLBNU
  https://www.youtube.com/watch?v=mKXLTchmay0
  We are going to make a machine to do this practicing procedure without this coach.

## Slide 9
  How to Make/Build Combinations?
  Players have freedom to build their fighting combinations in the opinion of their own.
  Recommended by the expert players
  What is the Novelty?
  While many fighters train with a punching bag, it's not really a fair fight – after all, the bag can't punch back. But this machine can do that.

## Slide 10: Project Aim & Objectives
Aim:
Design and develop an automated machine to practice boxing without a coach.
Objectives:
To guide the player to punch the correct positions.
To improve player's muscle memory
To practice alone without an opponent player or a trainer.
To practice a particular punch.
To practice more fighting techniques.
To improve the safety of the beginners.

## Slide 11: Proposed Solution (3D Model)
Head
Servo motors
Body
LCD Display
Metal Frame
DC motors
and wheels
Arms
Ultrasonic sensor
Keypad
PIR sensors
Stepper motor
LED lights and Piezo sensor

## Slide 12
3D Animation :-https://drive.google.com/file/d/12pWCA-nztkhnYb5SVaMTakm1cSb0yxxD/view?usp=sharing
Fitness band with heartbeat sensor

## Slide 14: Proposed Solution-System Diagram

## Slide 15: Schematic Diagram

## Slide 16: PCB Design
PCB design for machine side

## Slide 17: PCB design for Fitness Band

## Slide 18: Boxing Fighting Techniques(Combinations)
Combination 1
Step 1 – Jab (Punch by lead arm)
Step 2 – Cross (Punch by back arm)
Step 3 – Slip to Right (Move body to right)
Step 4 – Roll to Right (Walk to right)
Step 1- Jab

## Slide 19
Step 3- Slip to Right
Step 2- Cross

## Slide 20
Step 4- Roll to Right

## Slide 21: Combinations (Continue..)
Combination 2
  Jab
  Cross
  Slip to left
  Left hook-Head (Punch to left side of head)
  Cross
  Right block (Block right horizontal arm from player’s right hand)
  Left hook- Head

## Slide 22
Step 1-Jab
Step 2-Cross
Step 3-Slip to left

## Slide 23
Step 4-Left hook-Head
Step 5-Cross

## Slide 24
Step 6- Right block
Step 7-Left hook- Head

## Slide 25: Combination 3
Right upper cut (Punch to opponent player’s chin by right hand)
Left hook-Head
Cross
Block right
Slip to left
Left hook- Body
Left hook- Head
Cross
Slip to right

## Slide 26: Resource Required
Software: Atmel Studio, Blender, Proteus,
Hardware:
Sensors: Motion sensor, Piezo Sensor, Ultrasonic Sensor,Heartbeat Sensor
Microcontroller: Atmega32
Bluetooth Module
Motors: Stepper Motors, Servo Motors, Dc Motors
LCD display
Keypad
LED lights
Power supply unit
Rubber tyre wheels

## Slide 27
Cost Estimation
Name | Unit Price (Rs) | Quantity | Amount
At mega 32 microcontroller | 660.00 | 3 | 1980.00
Servo Motor | 600.00 | 5 | 3000.00
Motion Sensor | 250.00 | 2 | 500.00
Piezo Sensor | 25.00 | 6 | 150.00
LED light | 30.00 | 5 | 150.00
Keypad & key | 200.00 | 1 | 200.00
Ultrasonic Sensor | 370.00 | 2 | 740.00
Heartbeat Sensor | 650.00 | 1 | 650.00
Stepper Motor | 1800.00 | 1 | 1800.00
DC Gear Motor | 700.00 | 2 | 1400.00
LCD display | 550.00 | 1 | 550.00
Rexene | 510.00 | 2 meters | 1020.00
Sponge sheet | 600.00 | 2 | 1200.00
Box bar | 100.00 | 12 feet | 1200.00
Rubber tire wheels | 60.00 | 2 | 120.00
L293D DC motor driver | 490.00 | 2 | 980.00
ULN2003 Stepper Motor driver | 200.00 | 1 | 200.00
HC-05 Bluetooth Module | 1000.00 | 2 | 2000.00
Others |  |  | 2000.00
Total |  |  | 19840.00

## Slide 28: Testing and implementation
First ultrasonic sensor will measure the distance between player and the machine. Then stepper motor will adjust the machine according to the players height.

## Slide 29
Player can enter the technique number which he is willing to practice. Then the machine will work according to user entered technique (combination). Servo motor will move the arms of the machine according to user entered technique.

## Slide 30
Led lights used to indicate the punching positions. Piezo sensor will detect the punch and according to that LED will get off and next punching position will be indicated

## Slide 31
If the player wears the fitness band, then the sensor will measure the heart rate of the player and it will be displayed in the lcd display via Bluetooth.

## Slide 32
When first PIR sensor detects a motion, dc motors start to rotate clockwise. When second PIR sensor detects a motion, dc motors start to rotate anticlockwise.

## Slide 33
We developed the Full circuit using Proteus and Microchip Studio

## Slide 34
Individual Contribution

## Slide 35: Member 1 - Gamage T.T.P.D (204059X)
Responsibilities-
Piezo sensor and programming.
LCD Display and programming.
Design power supply unit.

## Slide 36: Piezo Sensor
Six piezo sensors use to detect the punch of the boxing player.
Identify the punch that the player made, by voltage produced in sensor.
Then the machine guides the player to punch the most suitable position for the next attack by lighting LED bulbs in sequence according to each technique.
Positive pin
Negative pin

## Slide 37
LED lights are used to guide the player. Led lights are placed in an unbreakable glass cover to protect them from players’ punch. If not, the lights can get broken. These lights indicate the place that the player wanted to punch. If the player punches to the place which the light indicates then the piezo detect the punch and the LED turns off. Then the next LED will turn on where the player wanted to punch next. Likewise, lights turn on in order according to the combination that the player selects.
LED lights and Piezo sensors

## Slide 38: Technique
Working of piezo sensor
A sensor which works on the principle of Piezoelectricity is known as Piezoelectric Sensor.

## Slide 39: Specification
●Maximum current 15mA;
●Voltage:≤30Vdc;
●Operating temperature:-20°C~+60°C
●Storage temperature:-30°C~+70°C
●Low Soldering temperature
●Strain sensitivity: 5V/µƐ
●Material: Quartz (mostly used)
Link for data sheet-
https://drive.google.com/file/d/14vjLFLfDX9N1wBRuEbYhlYJ7Q3bt68cu/view?usp=sharing

## Slide 40: Schematic Diagram

## Slide 41
Piezo Sensor Code

## Slide 42: LCD Display
We use LCD display to show boxing techniques as well as relevant details of the punch and boxing player. Player can select any technique according to their desire. In our project, we use LCD display on 8-bit mode

## Slide 43: Internal Structure
16 columns and 2 rows.
Display 32 alphanumeric characters at a time.
Each character is shown in pixels in 5x8 dot format.
Two modes – command mode and data mode
Two different modes – 8 bit mode and 4 bit mode
    Two operations -
    1. Read-can write any text to lcd.
    2. Write-can read data from lcd

## Slide 44: Specification
Operating Voltage is 4.7V to 5.3V
Current range 1.5mA – 2.3mA
Alphanumeric LCD display module, meaning can display alphabets and numbers
Consists of two rows and each row can print 16 characters.
Each character is built by a 5×8 pixel box
Can work on both 8-bit and 4-bit mode
It can also display any custom generated characters
Available in Green and Blue Backlight
Link for data sheet-
https://drive.google.com/file/d/180FnRGq6rmBGp0QE8G3knLvxweZjrY5J/view?usp=sharing

## Slide 45: Schematic Diagram

## Slide 46: PCB Design - Piezo Sensors and LCD Display

## Slide 47: Code for LCD Display

## Slide 49: Power Supply
1.Stepping down the Voltage Levels
  Use step-down transformer to convert 230V AC power supply into 12V AC.
2.Rectifying the signal
  12V AC current convert to DC current
3. Filter the signal
  Capacitor is used to filter(smooth) the signal.
4.Regulating DC Voltage
  A regulator IC is used for maintaining the constant DC output
There are four main steps in creating 5V and 12V dual DC power supply from the 230V AC main supply.

## Slide 50: Schematic Diagram

## Slide 51: PCB Design

## Slide 52: Member 2 - Kavishka T.A. (204101V)
Responsibilities :
4 Servo motors and programming.
Keypad and programming.
Programme fighting techniques.

## Slide 53: Servo Motor
Maximum voltage - 6V
Maximum current - 250mA
Link for datasheet: https://datasheetspdf.com/sg90

## Slide 54
The robot has 4 arms that move with the help of servo motors. These 4 arms can move in 90 degrees
These four arms act as the arms of the opposing player.
Motion Mechanism of Arms
Servo Motors

## Slide 55: 4x4 Keypad
4x4 Keypad has 8 pins 4 pins for columns and 4 pins for rows.
Maximum Voltage - 35V DC
Maximum current - 100mA
Link for datasheet: https://robocombo.com/uploads/Dosyalar/4x3-matrix-membrane-tus-takimi-datasheet.pdf

## Slide 56: Keypad internal view
Keypad use to input boxing techniques.
Keypad

## Slide 57: Servo Motor Codes

## Slide 59: Keypad Codes

## Slide 61: Circuit Diagram

## Slide 62: PCB Design

## Slide 63: Member 3 - Nuska M.F.F. (204145H)
Responsibilities
Heartbeat sensor and programming
Bluetooth module and programming
Designing the Fitness Band

## Slide 64
A fitness band that consists of a heartbeat sensor is used to measure the heart rate of the player.
Bluetooth module is used to transfer the data from the sensor to the LCD display.
Bluetooth module in the fitness band transfer the heart rate of the player to the machine through serial communication
Fitness Band

## Slide 65: Heartbeat Sensor
Maximum Current : 4mA
Maximum voltage : 5.5v
Model : SEN- 11574
Operating Temperature Range: -40°C to 85°C
Link for datasheet :
https://media.digikey.com/pdf/Data%20Sheets/Pulse%20Sensor%20PDFs/Pulse_Sensor.pdf
Heart beat sensor

## Slide 66: Technique
measure pulse waves by emitting red or infrared light from the body surface
detect the change in blood flow during heart beats as a change in the amount of light transmitted through the body.

## Slide 67: Heartbeat sensor circuit diagram

## Slide 68: Code for heartbeat sensor

## Slide 69: Bluetooth Module
HC 05 Bluetooth is a wireless communication protocol; it is used in two devices as a sending and receiving the information.
Bluetooth is free to use in the wireless communication
Bluetooth operates at the frequency of the 2.41 GHz
HC-05 module has two modes :
1. Data mode: Exchange of data between devices.
2. Command mode: It uses AT commands which are used to change setting of HC-05. To send these commands to module serial (USART) port is used.

## Slide 70: Technique
Bluetooth uses a technique known as frequency-hopping spread spectrum (FHSS), where the data is divided into chunks and transmitted via a carrier that hops from one random frequency to another.
Data is transmitted at a 1-Mbps rate using FSK.

## Slide 71: HC 05 Bluetooth Module
Specifications:
Operating Voltage: 4V to 6V (Typically +5V)
Maximum Current: 40mA
Model: HC-05
Communication Method: Serial Communication
can switch between master mode and slave mode
Transmission Distance :10m
Link to data sheet :
https://components101.com/sites/default/files/component_datasheet/HC-05%20Datasheet.pdf

## Slide 72: Pin description

## Slide 73: Code for HC 05 Bluetooth module

## Slide 74: Circuit diagram

## Slide 75: Member 4- Siriwardena P.T.Y. (204203K)
Responsibilities:-
Design a mechanical system to move the machine
DC gear motor and programming
PIR sensor and programming

## Slide 76: PIR Sensor

## Slide 77
Maximum Voltage :- 20V
Maximum Current :-50uA
Sensing range :- 120 degree
Data Sheet :-https://www.mpja.com/download/31227sc.pdf
PIR

## Slide 78: DC Motor
Maximum Voltage :- 15V
Maximum Current :- 1.2A
Stall torque:- 15N/cm @12V
Free-run speed:- 295 RPM @ 12V
DC Motor Data Sheet :- https://www.handsontec.com/dataspecs/motor_fan/JGB37-Geared%20Motor.pdf

## Slide 79: Application
DC Motor and Wheel

## Slide 80
Moving Process
Free area

## Slide 82: Circuit Diagram

## Slide 83: Member 5 - Ekanayaka Y.M. (204239B)
Stepper motor and programming.
Ultrasonic sensor and programming.
Design implementation of stepper motor and circuit diagram.
Integrate sub codes and implement final code.

## Slide 84: Stepper Motor
Bipolar stepper motor has 5 pins one for input power and others for control the motor, through the driver.
Maximum current -:1.7A
Maximum Voltage-:12V
Lint for datasheet-:https://www.datasheet4u.com/datasheet-pdf/MotionKing/17HS4401/pdf.php?id=928661

## Slide 86: Ultrasonic sensor
Maximum voltage-:5V
Maximum current-:15mA
Link for datasheet-:
https://datasheetspdf.com/pdf/1380136/ETC/HC-SR04/1

## Slide 88: Height Adjustment
Detect the height of the player by signal difference of ultrasonic sensors.

## Slide 89
This part is used to adjust the height of the machine according to the player’s height.
The cog which is in the stepper motor rotates according to the ultrasonic sensor detection. And the cog in the machine rotates according to the cog in the stepper motor and the screw in the bottom of the machine adjusts the height.
Screw thread and nut
Machine upper body
Cogs
Stepper motor

## Slide 90: Circuit diagram

## Slide 91: Codes for stepper motor and HC-SR04

## Slide 92: References
https://www.electronicwings.com/avr-atmega/inside
https://microchip.lk/
https://tronic.lk/
https://blog.joinfightcamp.com/training/six-6-basic-boxing-punches/
https://www.self.com/gallery/basic-boxing-moves
https://www.coolthings.com/stryk-rxt-1-sparring-robot-boxing-trainer/
https://www.youtube.com/watch?v=6VBIuqjLBNU
https://www.youtube.com/watch?v=mKXLTchmay0
https://www.youtube.com/watch?v=jhcIjFgz2bI

## Slide 93
Thank You!
Questions?